Pages in this namespace:
- Elektroinstallation 2022
- Infrastructure
- MQTT Server
- SpaceComputer
- SpaceLDAP
- WLAN
# Infrastructure
Diese und weitere Seiten im Namespace „it“ befinden sich in Restrukturierung und sind WIP
Das Netzwerk ist im IP-Bereich 10.0.0.0/8
## DHCP
Der DHCP läuft im Router und verteilt Adressen im Range 10.10.0.0 bis 10.10.2.255. Die Netzmaske ist 255.0.0.0. Standardgateway ist
router.vspace (10.0.0.1)
## AccessPoints
User aktuller AP ist der Ubuquiti UAP AC Lite und lässt sich über den controller auf Unifi verwalten
## DNS
Es wird der PFSense-interne DNS verwendet, welcher unter 10.0.0.1 erreichbar ist.
### Serversettings
Use the following as /etc/resolv.conf:
Warning: Only if you have not installed resolvconf. Otherwise this file is managed by resolvconf!
domain vspace
search vspace
nameserver 10.0.0.1
nameserver 8.8.8.8
Use the following /etc/network/interfaces part:
Warning: Only if the server has no tools like networkmanager installed! Otherwise this file is managed by networkmanager!
address 10.0.0.xxx
netmask 255.0.0.0
gateway 10.0.0.1
For setting the Hostname on the server you should replace the following in your /etc/hosts to:
127.0.1.1	servername.vspace	servername
## Probleme
### Analyse für Linux
Führe
dig ns02.vspace
und
dig @10.1.0.16 ns02.vspace
aus. Werden im zweiten Fall Antworten angezeigt und im ersten Fall nicht, verwendet dein PC den falschen DNS Server. Gibt als nächstes:
cat /etc/resolve.conf
ein. Hier werden die verwendeten Nameserver aufgelistet. Ist dein Nameserver 127.0.1.1 oder 127.0.0.1 gehe weiter zum entsprechenden Fehler.
### Nameserver 127.0.1.1
The 127.0.1.1 entry is most likely placed there by dnsmasq which is a local daemon for serving (and crucially caching) dns and dhcp. It's possible to configure NetworkManager to not run dnsmasq as follows: edit the file /etc/NetworkManager/NetworkManager.conf and comment out the line dns=dnsmasq by placing a # at the beginning of the line.
sudo nano /etc/NetworkManager/NetworkManager.conf
Now restart NetworkManager:
sudo service network-manager restart
Next check that the 127.0.1.1 entry has vanished from
/etc/resolv.conf
and replaced with those obtained from your router.